## Slide 1
FX45
I2C
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
BAC Wiring (No extenders up to one meter)
Use middle i2c header
And ensure VCCIO jumper is set to pins 2-3 (3.3V)

## Slide 2
FX45
I2C
BAC Wiring (With extenders)
FX14-mini
FX14-mini
FX14-mini
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Long ethernet cable
Short JST cable
Use hi drive i2c header
And ensure VCCIO jumper is set to pins 1-2 (5V)
JST Cable
Ethernet
Diagram incomplete, need hi drive -> ethernet wiring from ERT

## Slide 3
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
Microcontroller Wiring (No extenders up to one meter)
Cable pinout:
Pin 1: SCL
Pin 2: SDA
Pin 3: 3.3V+
Pin 4: Ground
SCL
SDA
3.3V+
GND
Microcontroller
2.2K pullup resistor on SCL and SDA
Pin 1 is square pad on hall sensor

## Slide 4
FX14-mini
Microcontroller Wiring (With extenders)
Cable pinout:
Pin 1: SCL
Pin 2: SDA
Pin 3: 3.3V+
Pin 4: Ground
SCL
SDA
3.3V+
GND
Microcontroller
2.2K pullup resistor on SCL and SDA
Pin 1 is square pad on hall sensor
FX14-mini
FX14-mini
FX14-mini
Alchemy Escape
3D Hall Sensor
Alchemy Escape
3D Hall Sensor
JST Cable
Ethernet
Long ethernet cable
Short JST cable